_display_2 timing

Clock for the one wire link.

Synchronise 9.6K data stream to 16MHz CPU frequency.

UNO (328) Use timer zero with times 8 prescaler giving a 2MHz clock.
Counts to 208.

ATtiny 1606 also offers a times 8 prescaler

Timing

Set WPU on com port
Set slow clock tick rate AND call Display_driver(0);
Tick 1	call Display_driver(1);
Tick 2	call Display_driver(2);
Tick 3	call Display_driver(3);

Tick 7	call Display_driver(7); AND set fast clock tick rate and issue start bit
Tick 8	send bit 0
Tick 9	send bit 1

Tick 15	send bit 7
Ticks 16 – 24	receive start bit and 8 data bits and wait 0.5 clock cycle then WPU

Repeat with slow clock tick AND Display_driver(0);

Timing

Start TCA	for loop controls display of digits 0 to 6
Initiate first / display tick	m= 0	m= 1	m= 2,3 and 4	m= 5	m= 6	m = 7
Set Comms port to WPU	Drive digit[0] and wait for tick	Drive digit[1] and wait for tick	Drive digits 2,3 and 4	Drive digit[5] and wait for tick	Drive digit[6] and wait for tick	Drive digit[7]
	Initiate next / display tick	Initiate next / display tick		Initiate final / display tick		Exit and call comms subroutine

Start TCA0	for loop controls display of digits 0 to 6
Initiate first / display tick	wait for first tick	wait for tick		wait for tick	wait for tick
Drive digit[0]	Drive digit[1]	Drive digit[2]	Drive digits 3,4 and 5	Drive digit[6]	Drive digit[7]
Set Comms port to WPU	Initiate next / display tick	Initiate next / display tick		Initiate next / display tick	Initiate comms tick issue start pulse / Call comms subroutine