_display_2 timing

Clock for the one wire link.

Synchronise 9.6K data stream to 16MHz CPU frequency.

UNO (328) Use timer zero with times 8 prescaler giving a 2MHz clock.
Counts to 208.

ATtiny 1606 also offers a times 8 prescaler

Timing

Set WPU on com port
Set slow clock tick rate AND call Display_driver(0);
Tick 1	call Display_driver(1);
Tick 2	call Display_driver(2);
Tick 3	call Display_driver(3);

Tick 7	call Display_driver(7); AND set fast clock tick rate and issue start bit
Tick 8	send bit 0
Tick 9	send bit 1

Tick 15	send bit 7
Ticks 16 – 24	receive start bit and 8 data bits and wait 0.5 clock cycle then WPU

Repeat with slow clock tick AND Display_driver(0);

Display/comms timing

1606:	16MHz clock 8MHz prescaler gives 2MHz peripheral clock

In a 2mS display period it counts to 4000.

4800	417	2ms
For a	9600 baud rate it counts to	208	Transaction time is	1ms
19200	104	0.52
28800	69	0.35
38400	52	0.26

328:	16MHz clock Use x8 or x64 prescalers giving 2MHz or 0.25MHz clocks.

For a	4800 baud rate it counts to	417 or 52 (0.25MHz clock)
9600	208 or 26

Experimental set up:
328 has a 0.25MHz timer clock and counts to 20 giving a baud rate of 12.5K
1606 has a 0.25MHz timer clock and counts to 28 Experimental value; (0.35MHz clock 22.4MHz free running clock??)

1606 0.5 second period 2MHz Peripheral clock x64 prescaler gives 31.25KHz clock which counts to 15625 in 0.5 s
(Note counting to 21875 gives a 0.5 second period.
Prescaler clock is 43.75KHz rather than 31.25KHz
Peripheral clock is 2.8MHz rather than 2MHz.)

assumes a clock of 43.75Hz 22.4MHz)

9600 Baud rate	1606 has peripheral clock of 2.8MHz Count to 292 rather than 202